## Slide 1: Atrazine Method CIPAC Collaborative Trial (5216/R) Germany (June 2019)
William Meyerhoffer, Nancy Shi

## Slide 2: Presentation Overview
General Information
Atrazine Method for TC; WG and SC formulations
Participants
Samples
Statistical Evaluation
Conclusion

## Slide 3: General Information
Atrazine
ISO common name: Atrazine
Chemical Name: 2-chloro-4-ethylamino-6-isopropylamino-s-triazine
Molecular mass: 215.7 g/mole
Empirical formula: C8H14ClN5
Structure:
Method quantitates Atrazine in technical material (TC) and in associated formulations [water dispersible granules (WG); suspension concentrate (SC)]
Atrazine peak resolved from internal standard and any potential sample matrix interferences (by-products, formulation components) by use of suitable chromatographic conditions

## Slide 4: General Information
Two TC’s and two formulation types (WG, SC) were analyzed for Atrazine content
Participants received samples and testing protocol including details on proposed gas chromatographic conditions and information on calculations and reporting of Study results
Any deviations from the proposed Atrazine method conditions were noted by the participating laboratories

## Slide 5: Determination of Atrazine in TC and WG, SC Formulations CIPAC Full Scale Collaborative Study (5216/R)

## Slide 6: Outline of Atrazine Method
The sample containing Atrazine is dissolved in acetone containing an internal standard (dipropyl phthalate)
Sample solution is sonicated and then filtered (PTFE) into vials for analysis
The Atrazine concentration is determined by capillary gas chromatography using split injection and flame ionization detection with internal standard calibration
Results reported in g/kg to one decimal place

## Slide 7: Proposed Atrazine Method Conditions
Capillary GC Column:
Fused silica, length 15 m x 0.25 mm internal diameter; DB-225 or equivalent phase, with film thickness of 0.25 m
(50% Cyanopropylphenyl/50% dimethylpolysiloxane).
Oven Temperature (Isothermal): 175°C
Flow : Hydrogen 2 mL/min
Contant Pressure Mode: 10 psi
Split: 50:1
Retention Times:
  Atrazine: 9 min. approximately
  Dipropyl Phthalate Internal Standard (IS): 6 min. approximately
  RRT of Atrazine/Internal Standard: approximately 1.5

## Slide 8: Method Calculations
Response factor RF
FC = Peak area of the reference substance on the reference chromatogram WC = Weight of the reference substance in mg, corrected for purity FCI = Peak area of the internal standard on the reference chromatogram WCI = Weight of the internal standard for the reference solution
Content (%); expressed in g/kg units for collaborative study
FS = Peak area of the active ingredient on the test chromatogram WS = Weight of the test substance FSI = Peak area of the internal standard on the test chromatogram WSI = Weight of the internal standard for the test solution

## Slide 9: Example Chromatogram – TC DB-225 Column (15 m x 0.25 mm, 0.25 µm)

## Slide 10: Example Chromatogram – WG Formulation DB-225 Column (15 m x 0.25 mm, 0.25 µm)

## Slide 11: Example Chromatogram – SC Formulation DB-225 Column (15 m x 0.25 mm, 0.25 µm)

## Slide 12: Example TC Chromatogram DB-1701 Column (30 m x 0.25 mm, 0.25 µm)
Consideration of DB-1701 as a potential alternative capillary GC column??
Atrazine
Internal
Standard

## Slide 13: Participants
Total of 20 respondents to CIPAC information sheet 318
  Sample set was sent to 16 participants
15 participants have sent back results in time
Participants were from Asia, Europe and the Americas
  Belgium, China, Germany, Greece, India, Ireland, Japan, Panama, Romania, Switzerland, Thailand, Uruguay and USA

## Slide 14: Samples
Atrazine Technical Concentrate: TC Sample A
Atrazine Technical Concentrate: TC Sample B
Atrazine Water Dispersible Granule: WG Sample C
Atrazine Suspension Concentrate: SC Sample D
Atrazine Suspension Concentrate: SC Sample E
Dipropyl Phthalate Internal Standard
Atrazine Reference Standard (971 g/kg)

## Slide 15: Statistical Evaluation – Screening for Validity of Data
All method deviations, noted by the participants, were deemed not to affect the analytical results significantly
For all samples, graphs demonstrating
  all data
  outliers/stragglers
and…..
Summary of statistical evaluation
  Including all data
  Mandel’s h and k straggler and outliers removed
Notes: Mandels test – inter-laboratory consistency: h  inter laboratory accuracy, k  within lab precision

## Slide 16: Statistical Evaluation – Outliers/Stragglers
Chart: Atrazine Sample A
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 13 | 14 | 15 | 16
 | 957.1 | 960.8 | 976.9 | 971.9 | 973.8 | 970.8 | 963.4 | 964.6 | 971 | 971.3 | 969.3 | 963.7 | 972.1 | 965 | 968.7
 | 971.6 | 967.8 | 998.9 | 972.5 | 974.1 | 972.3 | 968.4 | 972 | 972.2 | 972.3 | 972.8 | 967 | 972.5 | 966 | 968.9
 | 964.35 | 964.3 | 987.9 | 972.2 | 973.95 | 971.55 | 965.9 | 968.3 | 971.6 | 971.8 | 971.05 | 965.35 | 972.3 | 965.5 | 968.8
 | 970.3233 | 970.3233 | 970.3233 | 970.3233 | 970.3233 | 970.3233 | 970.3233 | 970.3233 | 970.3233 | 970.3233 | 970.3233 | 970.3233 | 970.3233 | 970.3233 | 970.3233
 | 985.2493 | 985.2493 | 985.2493 | 985.2493 | 985.2493 | 985.2493 | 985.2493 | 985.2493 | 985.2493 | 985.2493 | 985.2493 | 985.2493 | 985.2493 | 985.2493 | 985.2493
 | 955.3974 | 955.3974 | 955.3974 | 955.3974 | 955.3974 | 955.3974 | 955.3974 | 955.3974 | 955.3974 | 955.3974 | 955.3974 | 955.3974 | 955.3974 | 955.3974 | 955.3974
 | 989.8406 | 989.8406 | 989.8406 | 989.8406 | 989.8406 | 989.8406 | 989.8406 | 989.8406 | 989.8406 | 989.8406 | 989.8406 | 989.8406 | 989.8406 | 989.8406 | 989.8406
 | 950.8061 | 950.8061 | 950.8061 | 950.8061 | 950.8061 | 950.8061 | 950.8061 | 950.8061 | 950.8061 | 950.8061 | 950.8061 | 950.8061 | 950.8061 | 950.8061 | 950.8061
Atrazine TC – Sample A: 2 outliers detected
R limits
r limits
Mean
Mandel’s k-statistic and h-statistic outliers (Laboratory 3)
Notes: Straggler  5% level, assumes Gaussian
Outlier  1% level
R – reproducibility limit
r – repeatability limit
Error bars represent the two determinations on consecutive days

## Slide 17: Statistical Evaluation – Outliers/Stragglers
R limits
r limits
Mean
Atrazine TC – Sample B: 2 outliers and 1 straggler detected
Chart: Atrazine Sample B
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 13 | 14 | 15 | 16
 | 957.2 | 963.3 | 979.7 | 972.6 | 971.6 | 972.4 | 975.9 | 963.8 | 968.3 | 968.3 | 968.6 | 959.8 | 969.3 | 960.8 | 969
 | 971.4 | 967.7 | 982.3 | 972.8 | 971.9 | 975.5 | 976.5 | 969.2 | 971.6 | 969.5 | 970.9 | 976 | 969.6 | 962.3 | 994.1
 | 964.3 | 965.5 | 981 | 972.7 | 971.75 | 973.95 | 976.2 | 966.5 | 969.95 | 968.9 | 969.75 | 967.9 | 969.45 | 961.55 | 981.55
 | 970.73 | 970.73 | 970.73 | 970.73 | 970.73 | 970.73 | 970.73 | 970.73 | 970.73 | 970.73 | 970.73 | 970.73 | 970.73 | 970.73 | 970.73
 | 988.2863 | 988.2863 | 988.2863 | 988.2863 | 988.2863 | 988.2863 | 988.2863 | 988.2863 | 988.2863 | 988.2863 | 988.2863 | 988.2863 | 988.2863 | 988.2863 | 988.2863
 | 953.1737 | 953.1737 | 953.1737 | 953.1737 | 953.1737 | 953.1737 | 953.1737 | 953.1737 | 953.1737 | 953.1737 | 953.1737 | 953.1737 | 953.1737 | 953.1737 | 953.1737
 | 990.9264 | 990.9264 | 990.9264 | 990.9264 | 990.9264 | 990.9264 | 990.9264 | 990.9264 | 990.9264 | 990.9264 | 990.9264 | 990.9264 | 990.9264 | 990.9264 | 990.9264
 | 950.5336 | 950.5336 | 950.5336 | 950.5336 | 950.5336 | 950.5336 | 950.5336 | 950.5336 | 950.5336 | 950.5336 | 950.5336 | 950.5336 | 950.5336 | 950.5336 | 950.5336
Mandel’s k-statistic outlier and h-statistic straggler (Laboratory 16)

## Slide 18: Statistical Evaluation – Outliers/Stragglers
R limits
r limits
Mean
Atrazine WG – Sample C: 2 outliers detected
Chart: Atrazine Sample C
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 13 | 14 | 15 | 16
 | 892.8 | 887.1 | 909.7 | 884.7 | 884.4 | 885.9 | 891.8 | 868 | 883.6 | 883.2 | 884.2 | 880.1 | 893.3 | 880.5 | 885.9
 | 897.3 | 889.5 | 931.7 | 886.7 | 891.1 | 889.7 | 895.7 | 879.6 | 886.3 | 887.6 | 895.3 | 885.4 | 894.2 | 882.1 | 899.1
 | 895.05 | 888.3 | 920.7 | 885.7 | 887.75 | 887.8 | 893.75 | 873.8 | 884.95 | 885.4 | 889.75 | 882.75 | 893.75 | 881.3 | 892.5
 | 889.55 | 889.55 | 889.55 | 889.55 | 889.55 | 889.55 | 889.55 | 889.55 | 889.55 | 889.55 | 889.55 | 889.55 | 889.55 | 889.55 | 889.55
 | 906.3397 | 906.3397 | 906.3397 | 906.3397 | 906.3397 | 906.3397 | 906.3397 | 906.3397 | 906.3397 | 906.3397 | 906.3397 | 906.3397 | 906.3397 | 906.3397 | 906.3397
 | 872.7603 | 872.7603 | 872.7603 | 872.7603 | 872.7603 | 872.7603 | 872.7603 | 872.7603 | 872.7603 | 872.7603 | 872.7603 | 872.7603 | 872.7603 | 872.7603 | 872.7603
 | 920.5829 | 920.5829 | 920.5829 | 920.5829 | 920.5829 | 920.5829 | 920.5829 | 920.5829 | 920.5829 | 920.5829 | 920.5829 | 920.5829 | 920.5829 | 920.5829 | 920.5829
 | 858.5171 | 858.5171 | 858.5171 | 858.5171 | 858.5171 | 858.5171 | 858.5171 | 858.5171 | 858.5171 | 858.5171 | 858.5171 | 858.5171 | 858.5171 | 858.5171 | 858.5171
Mandel’s k-statistic and h-statistic outliers (Laboratory 3)

## Slide 19: Statistical Evaluation – Outliers/Stragglers
R limits
r limits
Mean
Atrazine SC – Sample D: 2 stragglers detected
Chart: Atrazine Sample D
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 13 | 14 | 15 | 16
 | 450.9 | 438 | 448.9 | 422.9 | 439.8 | 444.2 | 429.2 | 427.4 | 433.9 | 437.6 | 428.8 | 444.9 | 435.8 | 438.5 | 442.2
 | 451.3 | 440.8 | 450.9 | 428.4 | 444.6 | 446 | 430.6 | 429.9 | 440.7 | 440.2 | 439 | 456.1 | 439.1 | 440 | 450
 | 451.1 | 439.4 | 449.9 | 425.65 | 442.2 | 445.1 | 429.9 | 428.65 | 437.3 | 438.9 | 433.9 | 450.5 | 437.45 | 439.25 | 446.1
 | 439.6867 | 439.6867 | 439.6867 | 439.6867 | 439.6867 | 439.6867 | 439.6867 | 439.6867 | 439.6867 | 439.6867 | 439.6867 | 439.6867 | 439.6867 | 439.6867 | 439.6867
 | 450.3267 | 450.3267 | 450.3267 | 450.3267 | 450.3267 | 450.3267 | 450.3267 | 450.3267 | 450.3267 | 450.3267 | 450.3267 | 450.3267 | 450.3267 | 450.3267 | 450.3267
 | 429.0467 | 429.0467 | 429.0467 | 429.0467 | 429.0467 | 429.0467 | 429.0467 | 429.0467 | 429.0467 | 429.0467 | 429.0467 | 429.0467 | 429.0467 | 429.0467 | 429.0467
 | 463.2208 | 463.2208 | 463.2208 | 463.2208 | 463.2208 | 463.2208 | 463.2208 | 463.2208 | 463.2208 | 463.2208 | 463.2208 | 463.2208 | 463.2208 | 463.2208 | 463.2208
 | 416.1525 | 416.1525 | 416.1525 | 416.1525 | 416.1525 | 416.1525 | 416.1525 | 416.1525 | 416.1525 | 416.1525 | 416.1525 | 416.1525 | 416.1525 | 416.1525 | 416.1525
Mandel’s k-statistic stragglers (Laboratory 13)

## Slide 20: Statistical Evaluation – Outliers/Stragglers
Atrazine SC – Sample E: No outliers or stragglers detected
R limits
r limits
Mean
Chart: Atrazine Sample E
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 13 | 14 | 15 | 16
 | 433.2 | 433.1 | 441 | 429.3 | 437.3 | 442.5 | 431.5 | 426.1 | 433.5 | 435.3 | 426.3 | 438.2 | 434 | 433 | 437
 | 433.2 | 438 | 444.1 | 431.1 | 442.2 | 443.9 | 433.6 | 430.7 | 437.2 | 435.9 | 433.5 | 441.9 | 435.2 | 440.1 | 443.7
 | 433.2 | 435.55 | 442.55 | 430.2 | 439.75 | 443.2 | 432.55 | 428.4 | 435.35 | 435.6 | 429.9 | 440.05 | 434.6 | 436.55 | 440.35
 | 435.8533 | 435.8533 | 435.8533 | 435.8533 | 435.8533 | 435.8533 | 435.8533 | 435.8533 | 435.8533 | 435.8533 | 435.8533 | 435.8533 | 435.8533 | 435.8533 | 435.8533
 | 444.1708 | 444.1708 | 444.1708 | 444.1708 | 444.1708 | 444.1708 | 444.1708 | 444.1708 | 444.1708 | 444.1708 | 444.1708 | 444.1708 | 444.1708 | 444.1708 | 444.1708
 | 427.5359 | 427.5359 | 427.5359 | 427.5359 | 427.5359 | 427.5359 | 427.5359 | 427.5359 | 427.5359 | 427.5359 | 427.5359 | 427.5359 | 427.5359 | 427.5359 | 427.5359
 | 449.9922 | 449.9922 | 449.9922 | 449.9922 | 449.9922 | 449.9922 | 449.9922 | 449.9922 | 449.9922 | 449.9922 | 449.9922 | 449.9922 | 449.9922 | 449.9922 | 449.9922
 | 421.7145 | 421.7145 | 421.7145 | 421.7145 | 421.7145 | 421.7145 | 421.7145 | 421.7145 | 421.7145 | 421.7145 | 421.7145 | 421.7145 | 421.7145 | 421.7145 | 421.7145

## Slide 21: Summary of the Statistical Evaluation – No Elimination
Experimental result
Acceptance criterion
Notes: Key comparison is RSDR  relative reproducibility SD with RSDR(Hor)  relative reproducibility SD Horwitz calulation

## Slide 22: Summary of the Statistical Evaluation – Elimination of Outliers and Stragglers
Experimental result
Acceptance criterion

## Slide 23: Summary
With or without elimination of outliers or stragglers, the between laboratory experimental Relative Reproducibility Standard Deviation (% RSDR) is within the acceptance limit based on the Horwitz curve calculation (% RSDR(Hor)) for all samples tested (TC, WG and SC formulations)
% RSDR < % RSDR(Hor)

## Slide 24: Conclusion
We consider the method 5215/m to be suitably validated
We recommend that method 5215/m is considered as a provisional CIPAC method with potential inclusion of DB-1701 capillary GC column as an alternative to the proposed DB-225 column

## Slide 25
Special Thanks
To all laboratories and their staff participating in this collaborative trial and sending back the results in time……
Dr. Nancy Shi (Syngenta) for her assistance in the statistical analysis of all provided laboratory data.
Thank you