## Slide 1
Small Scale
Collaborative Trial
Ethephon
373

## Slide 2
Catalog
01
Background
02
New method introduction
04
Small scale trial results
05
Conclusion and recommendation
03
Single laboratory validation

## Slide 3
1. 1 General Information of Ethephon

## Slide 4
(i) Formation of ethephon disodium salt
Cl-CH2-CH2-P(O)(OH)2 + 2NaOH → Cl-CH2-CH2-P(O)(ONa)2 + 2H2O
(ii) Thermal decomposition of ethephon disodium salt
Cl-CH2-CH2-P(O)(ONa)2 + H2O → CH2=CH2 + NaCl + (HO)2P(O)(ONa)
(iii) Neutralisation of sodium dihydrogen phosphate
(HO)2P(O)(ONa) + NaOH → (HO)-P(O)(ONa)2 + H2O
1.2 Existing CIPAC Method-Titration(373/TK/M/- and 373/SL/M-)
Advantages:
  easy handling
  cost effectiveness
Challenges:
  Rely on person, less objective and stable
  Non-specific
The sample is neutralized to pH 9.3 to form the ethephon disodium salt, which is decomposed to ethene and sodium dihydrogen phosphate on heating. Sodium dihydrogen phosphate is determined by acidimetry.

## Slide 5
2.1 New method introduction-Ion Chromatography
Ethephon is determined by ion chromatography using electrolytic conductivity detector and external standardization. The analytical column used is based on alkanol quaternary ammonium.
Eluent: 7.2 mM Na2CO3 + 9.0 mM NaHCO3
Flow rate: 1.0 mL/min
Current of inhibitor: 70 mA
Temperature of detector cell: 35℃
Temperature of column: 30℃
Mode of injection: PushFull
Volume of Injection: 25μL
Frequency of data sampling: 5.0 Hz
Run time: 13 min
Retention time: 9.5 min
Chromatographic conditions (typical)
Apparatus

## Slide 6
Preparation of Calibration sample. Prepare sample solutions in duplicate. Weigh (to the nearest 0.1 mg) sufficient sample (w mg) to contain about 120 mg of Ethephon into a brown volumetric flask (100 ml). Add ultrapure water to the mark and mix thoroughly. Transfer 5.00 mL of the above solution into a 50 mL volumetric flask, add ultrapure water to the mark and mix thoroughly. (Calibration solutions CA and CB).
Preparation of Ethephon sample. Prepare sample solutions in duplicate for each sample. Weigh (to the nearest 0.1 mg) sufficient sample (w mg) to contain about 120 mg of Ethephon into a brown volumetric flask (100 ml) (For TC samples, heat the sample in 95 ℃ water bath to melt and mix well before weighing ). Add ultrapure water to the mark and mix thoroughly. Transfer 5.00 mL of the above solution into a 50 mL volumetric flask, add ultrapure water to the mark and mix thoroughly. (Sample solutions S1 and S2).
Determination. Inject in duplicate 25 μl portions of each sample solution bracketing them by injections of the calibration solutions as follows: calibration solution CA, sample solution S1, sample solution S1, calibration solution CB, sample solution S2, sample solution S2, calibration solution CA, and so on. Measure the relevant peak areas.
2.2 Procedure

## Slide 7
2.3 Calculation
Calculation. Determine the peak area of Ethephon and calculate the mean value of response factors from the calibration solutions bracketing the injections of the sample solutions and use this value for calculating the Ethephon content of the bracketed sample. The Ethephon content is the mean value of two sample solutions.
where:
fi = individual response factor
f = mean response factor of bracketing calibration injections
Hs = peak area of Ethephon in the calibration solution
Hw = peak area of Ethephon in the sample solution
s = mass of Ethephon reference standard in the calibration solution (mg)
w = mass of sample taken (mg)
P = purity of Ethephon reference standard (g/kg)

## Slide 8
3. Single lab validation
Ion Chromatography Method
Typical chromatograms and spectrum
Fig.2 HPIC chromatogram of Ethephon standard
SD
TC
TK
SL
NMR

## Slide 9
Performing lab: BioGuide Technologies Co., Ltd.
Chart: 
| 59.3 | 94.88 | 118.6 | 142.32 | 179.09
 | 1.3892 | 2.2376 | 2.8922 | 3.5135 | 4.5194
3.1 Linearity
Linearity range: 59.30-179.09 mg/L
R2=0.9992
Linearity of response

## Slide 10
3.2 Precision
Sample | Content |  |  |  |  | Mean content g/kg | RSD %
 | 1 g/kg | 2 g/kg | 3 g/kg | 4 g/kg | 5 g/kg |  | 
TC | 931.2 | 937.4 | 937.6 | 940.8 | 936.6 | 936.7 | 0.47
TK | 759.0 | 758.6 | 759.5 | 760.3 | 764.4 | 760.4 | 0.45
SL | 412.7 | 419.1 | 420.1 | 417.4 | 411.2 | 416.1 | 0.94
Precision test results for different samples

## Slide 11
3.3 Accuracy
Sample | Recovery |  |  |  | Mean recovery %
 | 1 % | 2 % | 3 % | 4 % | 
TC | 98.85 | 100.10 | 99.60 | 99.05 | 99.40
TK | 99.90 | 99.25 | 99.00 | 99.05 | 99.30
SL | 100.75 | 99.20 | 99.25 | 99.45 | 99.66
Accuracy test results for different samples

## Slide 12
4. Small scale trial results
4.1 Participants
NAME | ORGANIZATION
Xiangdong SHAO | BioGuide Technologies Co., Ltd.
Chunqing HOU | SYRICI (Shenyang Research Institute of Chemical Industry)
Xiaoying JI | Eastlake Hi-Tech

## Slide 13
4.2 Sample Information
Sample | Quantity | Batch | Declared Content of AI
ethephon TC1 | 50 g | E202011011 | Min. 93%
ethephon TC2 | 50 g | E202010030 | Min. 93%
ethephon TK1 | 50 mL | F202011011 | 75%
ethephon TK2 | 50 mL | F202010030 | 75%
ethephon SL1 | 50 mL | 2020110111 | 40%
ethephon SL2 | 50 mL | 2020100130 | 40%

## Slide 14
4.3 Results – TC1
Lab | Day1(%) |  | Day2(%) |  | Average Yi(%) | Standard Deviation Si(%) | RSD(%)
 | 1 | 2 | 1 | 2 |  |  | 
Lab1 | 93.32 | 93.38 | 93.25 | 93.20 | 93.29 | 0.0791 | 0.08
Lab2 | 94.22 | 94.02 | 93.88 | 93.94 | 94.01 | 0.1499 | 0.16
Lab3 | 94.02 | 94.54 | 93.86 | 94.31 | 94.18 | 0.3016 | 0.32
Table 1. Results of the analysis of AI content in the TC1

## Slide 15
Results – TC2
Lab | Day1(%) |  | Day2(%) |  | Average Yi(%) | Standard Deviation Si(%) | RSD(%)
 | 1 | 2 | 1 | 2 |  |  | 
Lab1 | 93.07 | 93.21 | 93.11 | 93.31 | 93.18 | 0.1091 | 0.12
Lab2 | 94.04 | 93.83 | 94.16 | 94.17 | 94.05 | 0.1587 | 0.17
Lab3 | 93.63 | 93.61 | 93.88 | 93.50 | 93.65 | 0.1609 | 0.17
Table 2. Results of the analysis of AI content in the TC2

## Slide 16
Results – TK1
Lab | Day1(%) |  | Day2(%) |  | Average Yi(%) | Standard Deviation Si(%) | RSD(%)
 | 1 | 2 | 1 | 2 |  |  | 
Lab1 | 76.47 | 77.55 | 76.17 | 76.65 | 76.71 | 0.5928 | 0.77
Lab2 | 76.24 | 75.82 | 75.51 | 76.01 | 75.90 | 0.3062 | 0.40
Lab3 | 75.99 | 76.20 | 76.01 | 76.03 | 76.06 | 0.0944 | 0.12
Table 3. Results of the analysis of AI content in the TK1

## Slide 17
Results – TK2
Lab | Day1(%) |  | Day2(%) |  | Average Yi(%) | Standard Deviation Si(%) | RSD(%)
 | 1 | 2 | 1 | 2 |  |  | 
Lab1 | 76.16 | 76.48 | 76.01 | 76.20 | 76.21 | 0.1940 | 0.25
Lab2 | 76.20 | 75.63 | 75.23 | 76.00 | 75.76 | 0.4268 | 0.56
Lab3 | 75.59 | 75.60 | 75.56 | 75.88 | 75.66 | 0.1503 | 0.20
Table 4. Results of the analysis of AI content in the TK2

## Slide 18
Results – SL1
Lab | Day1(%) |  | Day2(%) |  | Average Yi(%) | Standard Deviation Si(%) | RSD(%)
 | 1 | 2 | 1 | 2 |  |  | 
Lab1 | 41.18 | 41.28 | 41.28 | 41.14 | 41.22 | 0.0698 | 0.17
Lab2 | 41.74 | 41.65 | 41.22 | 40.84 | 41.36 | 0.4154 | 1.00
Lab3 | 40.80 | 40.43 | 41.01 | 41.10 | 40.84 | 0.3013 | 0.74
Table 5. Results of the analysis of AI content in the SL1

## Slide 19
Results – SL2
Lab | Day1(%) |  | Day2(%) |  | Average Yi(%) | Standard Deviation Si(%) | RSD(%)
 | 1 | 2 | 1 | 2 |  |  | 
Lab1 | 41.09 | 40.98 | 40.78 | 40.90 | 40.94 | 0.1351 | 0.33
Lab2 | 42.21 | 42.16 | 41.16 | 41.62 | 41.79 | 0.4960 | 1.19
Lab3 | 40.45 | 40.84 | 40.79 | 40.58 | 40.67 | 0.1811 | 0.45
Table 6. Results of the analysis of AI content in the SL2

## Slide 20
Summary of the Statistic results of all laboratories
 | TC1 | TC2 | TK1 | TK2 | SL1 | SL2
S1=sum Yi | 280.88 | 281.49 | 228.66 | 227.63 | 123.42 | 123.39
S2=sum Yi2 | 26297.82845 | 26412.20202 | 17429.21017 | 17272.07366 | 5077.75606 | 5075.71446
S3=sum Si2 | 0.0630 | 0.1197 | 0.4541 | 0.2424 | 0.2682 | 0.2971
No. Lab, P | 3 | 3 | 3 | 3 | 3 | 3
No. Determination, n | 4 | 4 | 4 | 4 | 4 | 4
Average Y=S1/P | 93.63 /936.3 | 93.83 /938.3 | 76.22 /762.2 | 75.88 /758.8 | 41.14 / 411.4 | 41.13 / 411.3
Sr | 0.1449 | 0.1997 | 0.3890 | 0.2843 | 0.2990 | 0.3147
SL | 0.4309 | 0.4648 | 0.3864 | 0.2594 | 0.2273 | 0.5616
SR | 0.4546 | 0.5059 | 0.5483 | 0.3848 | 0.3756 | 0.6438
r | 0.5593 / 5.593 | 0.4056 / 4.056 | 1.0893 / 10.893 | 0.7959 / 7.959 | 0.8371 / 8.371 | 0.8811 / 8.811
R | 1.4166 / 14.166 | 1.2729 / 12.729 | 1.5354 / 15.354 | 1.0774 / 10.774 | 1.0516 / 10.516 | 1.8025 / 18.025
RSDr | 0.2129 | 0.1547 | 0.5104 | 0.3746 | 0.7267 | 0.7651
SDR | 0.5392 | 0.4856 | 0.7194 | 0.5071 | 0.9129 | 1.5652
RSDR (Hor) | 2.0193 | 2.0199 | 2.0834 | 2.0849 | 2.2861 | 2.2862
HorRat | 0.27 | 0.24 | 0.35 | 0.24 | 0.40 | 0.68
Table 7. Statistics of the results

## Slide 21
Statistical formulas
Where:
Yi = mean of the various laboratories
Si = standard deviation
P = number of laboratories
n = number of measurements ( here n=4 )
x = average, in unit of g/kg
c = the concentration of the analyte as a decimal fraction

## Slide 22
4.4 Profits of ion chromatography method
Comparing with the existing titration method, ion chromatography method shows the following profits:
    High sensitivity and visualizability
    High reproducibility, and requiring less personal judgement and experience
    High specificity

## Slide 23
4.5 Comparison between existing and proposed methods
Sample | Existing Method | Proposed Method | SD | RSD (%)
TC1 | 930 | 937 | 4.95 | 0.53
TC2 | 931 | 941 | 7.07 | 0.76
TK1 | 755 | 757 | 1.41 | 0.19
TK2 | 756 | 761 | 3.54 | 0.47
SL1 | 403 | 407 | 2.83 | 0.70
SL2 | 404 | 408 | 2.83 | 0.70
Results using existing and proposed methods for different samples

## Slide 24
5. Conclusion and recommendation
Conclusion:
  For all samples, all values of RSDR were less than the calculated Horwitz value, and most of the HorRat values were between 0.3 and 1, while 3 values were less than 0.3, but quite near.
Recommendation:
  The method can be considered applicable to the determination of ethephon contents in TC, TK and SL.
  We propose that a full scale collaborative trial will be conducted.

## Slide 25
Thank you!
www.el-ht.com